Код програми.

/*****************************************************

This program was produced by the

CodeWizardAVR V2.04.4a Advanced

Automatic Program Generator

© Copyright 1998-2009 Pavel Haiduc, HP InfoTech s.r.l.

http://www.hpinfotech.com

Project :

Version :

Date    : 01.04.2012

Author  : NeVaDa

Company : Microsoft

Comments:

Chip type               : ATmega64

Program type            : Application

AVR Core Clock frequency: 8,000000 MHz

Memory model            : Small

External RAM size       : 0

Data Stack size         : 1024

*****************************************************/

#include <mega64.h>

#include <delay.h>

// Alphanumeric LCD Module functions

#asm

.equ __lcd_port=0x1B ;PORTA

#endasm

#include <lcd.h>

#ifndef RXB8

#define RXB8 1

#endif

#ifndef TXB8

#define TXB8 0

#endif

#ifndef UPE

#define UPE 2

#endif

#ifndef DOR

#define DOR 3

#endif

#ifndef FE

#define FE 4

#endif

#ifndef UDRE

#define UDRE 5

#endif

#ifndef RXC

#define RXC 7

#endif

#define FRAMING_ERROR (1<<FE)

#define PARITY_ERROR (1<<UPE)

#define DATA_OVERRUN (1<<DOR)

#define DATA_REGISTER_EMPTY (1<<UDRE)

#define RX_COMPLETE (1<<RXC)

// USART0 Receiver buffer

#define RX_BUFFER_SIZE0 8

char rx_buffer0[RX_BUFFER_SIZE0];

#if RX_BUFFER_SIZE0<256

unsigned char rx_wr_index0,rx_rd_index0,rx_counter0;

#else

unsigned int rx_wr_index0,rx_rd_index0,rx_counter0;

#endif

// This flag is set on USART0 Receiver buffer overflow

bit rx_buffer_overflow0;

// USART0 Receiver interrupt service routine

interrupt [USART0_RXC] void usart0_rx_isr(void)

{

char status,data;

status=UCSR0A;

data=UDR0;

if ((status & (FRAMING_ERROR | PARITY_ERROR | DATA_OVERRUN))==0)

{

rx_buffer0[rx_wr_index0]=data;

if (++rx_wr_index0 == RX_BUFFER_SIZE0) rx_wr_index0=0;

if (++rx_counter0 == RX_BUFFER_SIZE0)

{

rx_counter0=0;

rx_buffer_overflow0=1;

};

};

}

#ifndef _DEBUG_TERMINAL_IO_

// Get a character from the USART0 Receiver buffer

#define _ALTERNATE_GETCHAR_

#pragma used+

char getchar(void)

{

char data;

while (rx_counter0==0);

data=rx_buffer0[rx_rd_index0];

if (++rx_rd_index0 == RX_BUFFER_SIZE0) rx_rd_index0=0;

#asm("cli")

--rx_counter0;

#asm("sei")

return data;

}

#pragma used-

#endif

// USART0 Transmitter buffer

#define TX_BUFFER_SIZE0 8

char tx_buffer0[TX_BUFFER_SIZE0];

#if TX_BUFFER_SIZE0<256

unsigned char tx_wr_index0,tx_rd_index0,tx_counter0;

#else

unsigned int tx_wr_index0,tx_rd_index0,tx_counter0;

#endif

// USART0 Transmitter interrupt service routine

interrupt [USART0_TXC] void usart0_tx_isr(void)

{

if (tx_counter0)

{

--tx_counter0;

UDR0=tx_buffer0[tx_rd_index0];

if (++tx_rd_index0 == TX_BUFFER_SIZE0) tx_rd_index0=0;

};

}

#ifndef _DEBUG_TERMINAL_IO_

// Write a character to the USART0 Transmitter buffer

#define _ALTERNATE_PUTCHAR_

#pragma used+

void putchar(char c)

{

while (tx_counter0 == TX_BUFFER_SIZE0);

#asm("cli")

if (tx_counter0 || ((UCSR0A & DATA_REGISTER_EMPTY)==0))

{

tx_buffer0[tx_wr_index0]=c;

if (++tx_wr_index0 == TX_BUFFER_SIZE0) tx_wr_index0=0;

++tx_counter0;

}

else

UDR0=c;

#asm("sei")

}

#pragma used-

#endif

// Standard Input/Output functions

#include <stdio.h>

#define ADC_VREF_TYPE 0x00

// Read the AD conversion result

unsigned int read_adc(unsigned char adc_input)

{

ADMUX=adc_input | (ADC_VREF_TYPE & 0xff);

// Delay needed for the stabilization of the ADC input voltage

delay_us(10);

// Start the AD conversion

ADCSRA|=0x40;

// Wait for the AD conversion to complete

while ((ADCSRA & 0x10)==0);

ADCSRA|=0x10;

return ADCW;

}

void lcd_putfloat(float data, unsigned char row ,  unsigned char column)

{

char message[5];

unsigned int chuslo;

chuslo = (int) (data);

message[0] = chuslo + 0x30;

lcd_gotoxy(column, row);

lcd_putchar(message[0]);

message[1] = '.';

lcd_gotoxy(column + 1, row);

lcd_putchar(message[1]);

data = data - chuslo;

data = data * 10;

chuslo = (int) (data);

message[2] = chuslo + 0x30;

lcd_gotoxy(column + 2, row);

lcd_putchar(message[2]);

data = data - chuslo;

data = data * 10;

chuslo = (int) (data);

message[3] = chuslo + 0x30;

lcd_gotoxy(column + 3, row);

lcd_putchar(message[3]);

data = data - chuslo;

data = data * 10;

chuslo = (int) (data);

message[4] = chuslo + 0x30;

lcd_gotoxy(column + 4, row);

lcd_putchar(message[4]);

}

// Declare your global variables here

void main(void)

{

// Declare your local variables here

// Input/Output Ports initialization

// Port A initialization

// Func7=In Func6=In Func5=In Func4=In Func3=In Func2=In Func1=In Func0=In

// State7=T State6=T State5=T State4=T State3=T State2=T State1=T State0=T

PORTA=0x00;

DDRA=0x00;

// Port B initialization

// Func7=In Func6=In Func5=In Func4=In Func3=In Func2=In Func1=In Func0=In

// State7=T State6=T State5=T State4=T State3=T State2=T State1=T State0=T

PORTB=0x00;

DDRB=0x00;

// Port C initialization

// Func7=In Func6=In Func5=In Func4=In Func3=In Func2=In Func1=In Func0=In

// State7=T State6=T State5=T State4=T State3=T State2=T State1=T State0=T

PORTC=0x00;

DDRC=0x00;

// Port D initialization

// Func7=In Func6=In Func5=In Func4=In Func3=In Func2=In Func1=In Func0=In

// State7=T State6=T State5=T State4=T State3=T State2=T State1=T State0=T

PORTD=0x00;

DDRD=0x00;

// Port E initialization

// Func7=In Func6=In Func5=In Func4=In Func3=In Func2=In Func1=In Func0=In

// State7=T State6=T State5=T State4=T State3=T State2=T State1=T State0=T

PORTE=0x00;

DDRE=0x00;

// Port F initialization

// Func7=In Func6=In Func5=In Func4=In Func3=In Func2=In Func1=In Func0=In

// State7=T State6=T State5=T State4=T State3=T State2=T State1=T State0=T

PORTF=0x00;

DDRF=0x00;

// Port G initialization

// Func4=In Func3=In Func2=In Func1=In Func0=In

// State4=T State3=T State2=T State1=T State0=T

PORTG=0x00;

DDRG=0x00;

// Timer/Counter 0 initialization

// Clock source: System Clock

// Clock value: Timer 0 Stopped

// Mode: Normal top=FFh

// OC0 output: Disconnected

ASSR=0x00;

TCCR0=0x00;

TCNT0=0x00;

OCR0=0x00;

// Timer/Counter 1 initialization

// Clock source: System Clock

// Clock value: Timer1 Stopped

// Mode: Normal top=FFFFh

// OC1A output: Discon.

// OC1B output: Discon.

// OC1C output: Discon.

// Noise Canceler: Off

// Input Capture on Falling Edge

// Timer1 Overflow Interrupt: Off

// Input Capture Interrupt: Off

// Compare A Match Interrupt: Off

// Compare B Match Interrupt: Off

// Compare C Match Interrupt: Off

TCCR1A=0x00;

TCCR1B=0x00;

TCNT1H=0x00;

TCNT1L=0x00;

ICR1H=0x00;

ICR1L=0x00;

OCR1AH=0x00;

OCR1AL=0x00;

OCR1BH=0x00;

OCR1BL=0x00;

OCR1CH=0x00;

OCR1CL=0x00;

// Timer/Counter 2 initialization

// Clock source: System Clock

// Clock value: Timer2 Stopped

// Mode: Normal top=FFh

// OC2 output: Disconnected

TCCR2=0x00;

TCNT2=0x00;

OCR2=0x00;

// Timer/Counter 3 initialization

// Clock source: System Clock

// Clock value: Timer3 Stopped

// Mode: Normal top=FFFFh

// OC3A output: Discon.

// OC3B output: Discon.

// OC3C output: Discon.

// Noise Canceler: Off

// Input Capture on Falling Edge

// Timer3 Overflow Interrupt: Off

// Input Capture Interrupt: Off

// Compare A Match Interrupt: Off

// Compare B Match Interrupt: Off

// Compare C Match Interrupt: Off

TCCR3A=0x00;

TCCR3B=0x00;

TCNT3H=0x00;

TCNT3L=0x00;

ICR3H=0x00;

ICR3L=0x00;

OCR3AH=0x00;

OCR3AL=0x00;

OCR3BH=0x00;

OCR3BL=0x00;

OCR3CH=0x00;

OCR3CL=0x00;

// External Interrupt(s) initialization

// INT0: Off

// INT1: Off

// INT2: Off

// INT3: Off

// INT4: Off

// INT5: Off

// INT6: Off

// INT7: Off

EICRA=0x00;

EICRB=0x00;

EIMSK=0x00;

// Timer(s)/Counter(s) Interrupt(s) initialization

TIMSK=0x00;

ETIMSK=0x00;

// USART0 initialization

// Communication Parameters: 8 Data, 1 Stop, No Parity

// USART0 Receiver: On

// USART0 Transmitter: On

// USART0 Mode: Asynchronous

// USART0 Baud Rate: 9600

UCSR0A=0x00;

UCSR0B=0xD8;

UCSR0C=0x06;

UBRR0H=0x00;

UBRR0L=0x33;

// Analog Comparator initialization

// Analog Comparator: Off

// Analog Comparator Input Capture by Timer/Counter 1: Off

ACSR=0x80;

SFIOR=0x00;

// ADC initialization

// ADC Clock frequency: 1000,000 kHz

// ADC Voltage Reference: AREF pin

//ADMUX=ADC_VREF_TYPE & 0xff;

//ADCSRA=0x83;

ADMUX=ADC_VREF_TYPE & 0xff;

ADCSRA=0x82;

SFIOR&=0xEF;

// LCD module initialization

lcd_init(16);

// Global enable interrupts

#asm("sei")

while (1)

{

unsigned int chus = 0;

float data = 0;

char dani = getchar();

switch (dani)

{

case '1':

lcd_clear();

chus = read_adc(0);

data = chus*2.5/1024;

lcd_gotoxy(0,0);

lcd_puts("Dani z 1 kanalu");

lcd_putfloat(data, 1, 0);

chus = (int)data;

putchar('\n\r');

putchar('O');

putchar('K');

putchar('\n\r');

break;

case '2':

lcd_clear();

chus = read_adc(1);

data = chus*2.5/1024;

lcd_gotoxy(0,0);

lcd_puts("Dani z 2 kanalu");

lcd_putfloat(data, 1, 0);

chus = (int)data;

putchar('\n\r');

putchar('O');

putchar('K');

putchar('\n\r');

break;

case '3':

lcd_clear();

chus = read_adc(2);

data = chus*2.5/1024;

lcd_gotoxy(0,0);

lcd_puts("Dani z 3 kanalu");

lcd_putfloat(data, 1, 0);

chus = (int)data;

putchar('\n\r');

putchar('O');

putchar('K');

putchar('\n\r');

break;

case '4':

lcd_clear();

chus = read_adc(3);

data = chus*2.5/1024;

lcd_gotoxy(0,0);

lcd_puts("Dani z 4 kanalu");

lcd_putfloat(data, 1, 0);

chus = (int)data;

putchar('\n\r');

putchar('O');

putchar('K');

putchar('\n\r');

break;

};

};

}