VHDL-опису

| Текст VHDL-опису NOT | Текст VHDL-опису OR | Текст VHDL-опису AND | Текст VHDL-опису XOR |
| --- | --- | --- | --- |
| library IEEE; use IEEE.std_logic_1164.all; entity \NOT\ is port ( X: in STD_LOGIC; Y : out STD_LOGIC ); end \NOT\; architecture \NOT\ of \NOT\ is begin Y <=NOT X after 5ns; end \NOT\; | library IEEE; use IEEE.std_logic_1164.all; entity \OR\ is port ( X1: in STD_LOGIC; X2: in STD_LOGIC; Y : out STD_LOGIC ); end \OR\; architecture \OR\ of \OR\ is begin Y<=X1 OR X2 after 10ns; end \OR\; | library IEEE; use IEEE.std_logic_1164.all; entity \AND\ is port ( X1: in STD_LOGIC; X2: in STD_LOGIC; Y: out STD_LOGIC ); end \AND\; architecture \AND\ of \AND\ is begin Y<=X1 AND X2 after 10ns; end \AND\; | library IEEE; use IEEE.std_logic_1164.all; entity \XOR\ is port ( X1: in STD_LOGIC; X2: in STD_LOGIC; Y: out STD_LOGIC ); end \XOR\; architecture \XOR\ of \XOR\ is begin Y<=X1 XOR X2 after 10ns; end \XOR\; |
| Текст VHDL-опису NAND | Текст VHDL-опису NOR | Текст VHDL-опису XNOR |
| library IEEE; use IEEE.std_logic_1164.all; entity \NAND\ is port ( X1: in STD_LOGIC; X2: in STD_LOGIC; Y: out STD_LOGIC ); end \NAND\; architecture \NAND\ of \NAND\ is begin Y<=X1 NAND X2 after 10ns; end \NAND\; | library IEEE; use IEEE.std_logic_1164.all; entity \NOR\ is port ( X1: in STD_LOGIC; X2: in STD_LOGIC; Y: out STD_LOGIC ); end \NOR\; architecture \NOR\ of \NOR\ is begin Y<=X1 NOR X2 after 10ns; end \NOR\; | library IEEE; use IEEE.std_logic_1164.all; entity \XNOR\ is port ( X1: in STD_LOGIC; X2: in STD_LOGIC; Y: out STD_LOGIC ); end \XNOR\; architecture \XNOR\ of \XNOR\ is begin Y<=X1 XNOR X2 after 10ns; end \XNOR\; |
| Текст VHDL-опису Logic |
| library IEEE; use IEEE.std_logic_1164.all; entity Logic is port ( X: in STD_LOGIC_VECTOR (2 downto 0); Y: out STD_LOGIC ); end Logic; architecture Logic of Logic is component \NOT\ is port ( X: in STD_LOGIC; Y: out STD_LOGIC ); end component; component \OR\ is port ( X1: in STD_LOGIC; X2: in STD_LOGIC; Y: out STD_LOGIC ); end component; component \AND\ is port ( X1: in STD_LOGIC; X2: in STD_LOGIC; Y: out STD_LOGIC ); end component; | component \XOR\ is port ( X1: in STD_LOGIC; X2: in STD_LOGIC; Y: out STD_LOGIC ); end component; component \NAND\ is port ( X1: in STD_LOGIC; X2: in STD_LOGIC; Y: out STD_LOGIC ); end component; component \NOR\ is port ( X1: in STD_LOGIC; X2: in STD_LOGIC; Y: out STD_LOGIC ); end component; component \XNOR\ is port ( X1: in STD_LOGIC; X2: in STD_LOGIC; Y: out STD_LOGIC ); end component; | signal A:std_logic; signal B:std_logic; signal C:std_logic; signal D:std_logic; signal E:std_logic; signal F:std_logic; begin NOT2OR : \NOT\ port map (X(0),A); NOT2OR2: \OR\ port map (A, X(1), B); NOT2NOR: \NOR\ port map (A, X(2), C); BC2AND: \AND\ port map (B, C, D); XC2M2: \XNOR\ port map (C, X(2), E); BD2M2: \XOR\ port map (B, D, F); EF2NAND: \NAND\ port map (F, E, Y); end Logic; |

Структурні описи у Verilog.

| Визначення модуля Декларації портів Декларація внутрішнього сигналу Перший вентиль xor Перший вентиль and Вентиль xor суми Другий вентиль and Третій вентиль and Вихідний вентиль or | module FullAdd_1Bit (Sum,Cout,A,B,Cin); output Sum,Cout; input A,B,Cin; wire AxorB,AandB,AandCin,BandCin; xor #5 HalfSum (AxorB,A,B); and #4 (AandB,A,B); xor FullSum(Sum,AxorB,Cin); and #4 And_2 (AandCin,A,Cin); and #4 And_3(BandCin,B,Cin); or (Cout,AandB,AandCin,BandCin); endmodule |
| --- | --- |